MECH420 Lab 2
Ratthamnoon Prakitpong
#63205165

Part A: Characterization of the optical encoder signal

1.

Fig A1: Encoder signal for clockwise rotation
Clockwise rotation
Time (s)
Output (bool)

Fig A2: Encoder signal for counter-clockwise rotation
Counter-clockwise rotation
Time (s)
Output (bool)

2.
For clockwise rotation, channel A leads by 90 degrees. For counter-clockwise rotation, channel B leads by 90 degrees.

3.
The encoder generates 360 pulses per revolution per channel (N = 360). The encoder generates quadrature signals. Note that we substitute N with 4N into following equations because signals are quadrature.

Pulse counting method:
I counted the pulses, which is n in the equations. The equations for angular speed and its resolution are:

The calculated values are:

Table A1: Angular speed and resolution, pulse counting method

This method provides low accuracy at low speed, which is the case here. This method’s resolution is finer than pulse timing method’s resolution.

Pulse timing method:
I counted and calculated average clock count of one pulse in a data set, which is m in the equations. Frequency is 40000 Hz (I see 40 counts in 0.0001s). The equations for angular speed and its resolution are:

The calculated values are:
Table A2: Angular speed and resolution, pulse timing method

This method is better for low speed. The approximate resolution is closer to exact resolution at lower speed.

Part B: Characterization of the Torque Sensor

1.

Fig B1: Voltage vs Torque, both cycles

Arbitrarily, I used left weights as negative torque, so the plot resulted in a negative slope.

2.

Fig B2: Voltage vs Torque, second load cycles only

Calibration equation is taken from the plot above (numpy.polyfit uses least square method):
V(T) = b + mT, m = -6.174 V/Nm, b = V0 = 0.124 V

3.
We get nonlinear error with this equation:

Where theoretical value is value from regression, and experimental value is from averaging values.

We get hysteresis error with this equation:

Where I is the value we’re finding error of, and H is the percent error. Note that we also have to take absolute value of H to get satisfactory percent error.

We use average values for each values in the equations for calculations. Plotted, we get:

Fig B3: Percent errors at torque loads

4.
From the product datasheet I found online:

Theoretical calculations are shown in Part 5.2.

Sensitivity:
Theoretical:
Sensitivity = 0.728 mV/Nm

Experimental:
Slope from fig B2 = 6.174 V/Nm
Amplifier = 100
Sensitivity without gain from amplifier = 6.174 V/Nm / 100 = 61.74 mV/Nm

This is very suspect. Reason could be analysis error, or measurement error. For example, the unit for torque was given as Nm. However, the numbers felt suspiciously like they were supposed to be kgm (600 grams * 400 mm = 0.6 kg * 0.4 m = 0.24 kgm != 0.24 kgmm/(ss)). Not accounting for gravity can cause recorded torque values to be smaller than they actually are, hence larger sensitivity.

Offset:
Theoretical:
Offset = 4 mV

Experimental:
Y-intercept from fig B2 = 0.124 V
Amplifier = 100
Offset = 0.124V / 100 = 1.24 mV

It makes sense that we have some offset, but did not hit the maximum of how far off our data could be.

Absolute errors:
Theoretical:
Linearity error = 0.004 mV
Hysteresis error = 0.003 mV

Experimental:
We get these values from plot, multiplying percent error by experimental values.
Average most linearity error = 0.00295 mV
Average hysteresis error = 0.00109 mV

The theoretical value is in range of our theoretical calculations.

Part C: Measurement of the Torque Required to Drive the Conveyor

1.
Given that the belt ran two full cycles and that we want to plot one full cycle, we can just plot half the given data. Average torque and its standard deviation are included in the plot.

Fig C1: Torque over one full cycle of conveyor belt

5. Additional Exercises

1.

Speed is 1.74 rad/s.
2.

3.
Part	Datasheet
DC motor with encoder	https://media.digikey.com/pdf/Data%20Sheets/DFRobot%20PDFs/FIT0186_Web.pdf
Microcontroller	https://www.farnell.com/datasheets/1682209.pdf
PWM Amp	https://media.digikey.com/pdf/Data%20Sheets/DFRobot%20PDFs/DRI0002_Web.pdf

Appendix

e1-pulsecount-get_n.py
import os / dir_path = os.path.dirname(os.path.realpath(__file__)) / print(dir_path) / files = ['e1_motor_0.5V.csv', 'e1_motor_0.7V.csv', 'e1_motor_0.9V.csv'] / for name in files: / with open(dir_path+'\\'+name) as f: / counter = 0 / flag = False / for line in f: / items = line.split(',') / if len(items) > 1: / if items[1] == '1' and flag == False: / flag = True / counter = counter + 1 / if items[1] == '' and flag == True: / flag = False / print(name) / print(counter)

e1-pulsetiming-get_m.py
import os / dir_path = os.path.dirname(os.path.realpath(__file__)) / print(dir_path) / files = ['e1_motor_0.5V.csv', 'e1_motor_0.7V.csv', 'e1_motor_0.9V.csv'] / for name in files: / with open(dir_path+'\\'+name) as f: / counts = [] / counter = 0 / prev = '' / for line in f: / items = line.split(',') / if len(items) > 1: / if items[1] == '1' and prev == '': / counts.append(counter) / counter = 0 / counter = counter + 1 / prev = items[1] / print(name) / print(sum(counts[1:len(counts)])/(len(counts)-1))

e2.py
import os / import matplotlib.pyplot as plt / import numpy as np / dir_path = os.path.dirname(os.path.realpath(__file__)) / print(dir_path) / def plotter(files_right_, files_left, savename=None): / t_08 = [] # underscore == negative == left weights / t_16 = [] / t_24 = [] / t_32 = [] / t00 = [] / t08 = [] / t16 = [] / t24 = [] / t32 = [] / for name in files_right_: / with open(dir_path+'\\'+name) as f: / for line in f: / items = line.split(',') / if len(items) > 1: / if items[1] == '': / t00.append(float(items[2]) - float(items[3])) / if items[1] == '.08': / t08.append(float(items[2]) - float(items[3])) / if items[1] == '.16': / t16.append(float(items[2]) - float(items[3])) / if items[1] == '.24': / t24.append(float(items[2]) - float(items[3])) / if items[1] == '.32': / t32.append(float(items[2]) - float(items[3])) / for name in files_left: / with open(dir_path+'\\'+name) as f: / for line in f: / items = line.split(',') / if len(items) > 1: / if items[1] == '': / t00.append(float(items[2]) - float(items[3])) / if items[1] == '.08': / t_08.append(float(items[2]) - float(items[3])) / if items[1] == '.16': / t_16.append(float(items[2]) - float(items[3])) / if items[1] == '.24': / t_24.append(float(items[2]) - float(items[3])) / if items[1] == '.32': / t_32.append(float(items[2]) - float(items[3])) / x = [-0.32, -0.24, -0.16, -0.08, 0, 0.08, 0.16, 0.24, 0.32] / y = [sum(n)/len(n) for n in [t_32, t_24, t_16, t_08, t00, t08, t16, t24, t32]] / m, b = np.polyfit(x, y, 1) / if savename: / plt.clf() / plt.plot(x, y, 'bo--') / plt.title('Output voltage (V) vs Input Torque (Nm)\nm=' + str(m) + ',b=' + str(b)) / plt.ylabel('Output (V)') / plt.xlabel('Torque (Nm)') / plt.savefig(dir_path + '\\' + savename + '.png') / return y / def getHysteresisError(filename): / firstPass = [[], [], []] / secondPass = [[], [], []] / firstPassDone = False / for name in files_right_: / with open(dir_path+'\\'+name) as f: / for line in f: / items = line.split(',') / if len(items) > 1: / ind = 3 / if items[1] == '.08': / ind = 0 / if items[1] == '.16': / ind = 1 / if items[1] == '.24': / ind = 2 / if items[1] == '.32': / firstPassDone = True / if ind < 3: / val = float(items[2]) - float(items[3]) / if firstPassDone: / secondPass[ind].append(val) / else: / firstPass[ind].append(val) / avgFirstPass = [sum(n)/len(n) for n in firstPass] / avgSecondPass = [sum(n)/len(n) for n in secondPass] / #print(sum([abs(x) for x in [(f - s) for f, s in zip(avgFirstPass, avgSecondPass)]])/len(avgFirstPass)) # for part B4 / # take the two avg error, times each by 3, sum them, divide by 9 to get total avg / error = [100 * (f - s) / max(f, s) for f, s in zip(avgFirstPass, avgSecondPass)] / error = [abs(n) for n in error] / return error / # 1 / files_right_ = ['e2_torque_0.csv', 'e2_torque_one_by_one_right.csv', 'e2_torque_one_by_one_right_2.csv'] / files_left = ['e2_torque_one_by_one_left.csv', 'e2_torque_one_by_one_left_2.csv'] / plotter(files_right_, files_left, savename='e2-1') / #2 / files_right_ = ['e2_torque_one_by_one_right_2.csv'] / files_left = ['e2_torque_one_by_one_left_2.csv'] / plotter(files_right_, files_left, savename='e2-2') / #3 / files_right_ = ['e2_torque_one_by_one_right_2.csv'] / files_left = ['e2_torque_one_by_one_left_2.csv'] / x = [-0.32, -0.24, -0.16, -0.08, 0, 0.08, 0.16, 0.24, 0.32] / m = -6.174 / b = .124 / theory = [b + m*n for n in x] / real = plotter(files_right_, files_left) / print(sum([abs(x) for x in [(t - r) for t, r in zip(theory, real)]])/len(theory)) #for part B4 / nonlinearError = [100 * (t - r) / t for t, r in zip(theory, real)] / nonlinearError = [abs(a) for a in nonlinearError] / e_right = getHysteresisError(files_right_) / e_left = getHysteresisError(files_left) / e_left.reverse() / hysteresisError = [0] + e_left + [0] + e_right + [0] # 0s represent no hysteresis error at 0 and .32 Nm, where they are end points / plt.clf() / plt.plot(x, nonlinearError, 'bo--', label='Nonlinear error') / plt.plot(x, hysteresisError, 'go--', label='Hysteresis error') / plt.title('Errors (%) at torque loads (Nm)') / plt.ylabel('Percent error (%)') / plt.xlabel('Torque (Nm)') / plt.legend() / plt.savefig(dir_path + '\\' + 'e2-3.png')

e3.py
import os / import matplotlib.pyplot as plt / import numpy as np / dir_path = os.path.dirname(os.path.realpath(__file__)) / print(dir_path) / name = 'e3_50RPM.csv' / def file_len(fname): / with open(dir_path+'\\'+fname) as f: / for i, l in enumerate(f): / pass / return i + 1 / filelen = file_len(name) / t = [] / rpm = [] / cell0 = [] / cell1 = [] / with open(dir_path+'\\'+name) as f: / next(f) # discard first line / counter = 0 # to flush out initial data / startSaving = False / initTime = 0 / for line in f: / items = line.split(',') / counter = counter + 1 / if counter > filelen / 2: / t.append(float(items[0])) / rpm.append(float(items[1])) / cell0.append(float(items[2])) / cell1.append(float(items[3])) / m = -6.174 / b = .124 / T = [(c0 - c1 - b)/m for c0, c1 in zip(cell0, cell1)] / avgT = np.mean(T) / stdT = np.std(T) / plt.clf() / plt.plot(t, T) / plt.title('Torque (Nm) vs Time (s)\nAverage torque = ' + str(avgT) + ' Nm\nStandard deviation = ' + str(stdT) + ' Nm') / plt.ylabel('Torque (Nm)') / plt.xlabel('Time (s)') / plt.savefig(dir_path + '\\' + 'e3.png')